## Slide 1: Wireless Networks : Introduction
Overview of Wireless Networks
Based on material from several texts:
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
Computer Networks, fifth edition
Andrew Tanenbaum
Pearson Education/Prentice Hall
Notes: Last update: 11/3/2015

## Slide 2: Objectives
Fundamental principles behind wireless data communications
Design issues in wireless networks
Modern examples: WiFi, 3G/4G
Future directions
Relationship between applications and wireless networks

## Slide 3: OSI Reference Model (Tanenbaum)
A principled, international standard, seven layer model to connect different systems
– Provides functions needed by users
– Converts different representations
– Manages task dialogs
– Provides end-to-end delivery
– Sends packets over multiple links
– Sends frames of information
– Sends bits as signals

## Slide 4: TCP/IP Reference Model
A four layer model derived from experimentation; omits some OSI layers and uses the IP as the network layer.
IP is the “narrow waist” of the Internet
Protocols are shown in their respective layers
Notes: The comment about the narrow waist refers to the fact that the network layer of the Internet is IP (Internet Protocol) such that the network layer is called the “Internet” layer. The significance is that all Internet devices speak IP, which provides a point of interoperability that enables innovation both above (new applications and transports) and below (new link technologies).

## Slide 5: Chapter 6 outline (Kurose Text)
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 6: Elements of a wireless network
network
infrastructure

## Slide 7: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
network
infrastructure

## Slide 8: Elements of a wireless network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
network
infrastructure

## Slide 9: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 10: Elements of a wireless network
Acronym Roadmap
WiFi: (wireless lans): IEEE 802.11*
  DSRC (dedicated short range communications), uses extensions to 802.11a (called 802.11p)
Zigbee (sensor networks): IEEE 802.15
Cellular: 3G, 4G, and yes…5G.
  3G: many standards throughout the world but it generally refers to ‘Third Generation’ cellular systems that supports voice and data (i.e., smartphones with data rates of up to several hundred kbps)
  4G: distinguished from 3G by higher data rates (multiple Mbps). Two terms to note:
    WiMAX: Worldwide Interoperability for Microwave Access (standardarize by IEEE 802.16*) repesents the original direction for high speed wireless data
    LTE: Long Term Evolution is the 4G technology that was adopted by the cellular industry.
network
infrastructure

## Slide 11: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)

## Slide 12: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network
infrastructure

## Slide 13: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 14: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 15: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 16: Wireless Link Characteristics (1)
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 17: Wireless Link Characteristics (2)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoffs
  given physical layer: increase power -> increase SNR->decrease BER
  given SNR: choose physical layer that meets BER requirement, giving highest thruput
    SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 18: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 19: Objectives
Fundamental principles behind wireless data communications
Design issues in wireless networks
Modern examples: WiFi, 3G/4G
Future directions
Relationship between applications and wireless networks

## Slide 20: Maximum Data Rate of a Channel
Information (data) can be transmitted (sent) over a physical medium by representing data using voltage levels or by encoding the data in the frequency domain.
Physics defines how this works….
We abstract this complexity to:
  A channel represents the physical medium.
  Channel bandwidth (sometimes referred to as the capacity) refers to the portion of the medium used by the channel. We define this in units of Hertz (Hz).
    Bandwidth represents how frequently a sine wave can oscillate in the channel.
Notes: These are fundamental limits; real systems can only approach them.
S/N is called the signal to noise ratio SNR, and it is commonly measured in decibels on a logarithmic scale e.g., 10dB means the signal is 10X noise, 20dB means 100X noise, etc.

## Slide 21: Maximum Data Rate of a Channel
Nyquist’s theorem relates the data rate to the bandwidth (B) and number of signal levels (V):
Example: A coaxial medium (i.e., a cable network) has a total capacity of about 2 GHz.
  This is divided into small 6 MHz channels (Concept: frequency division multiplexing)
  Different modulations are supported that offer up to 256 signal levels
  Max data rate when assuming 64 signal levels: 2*6MHz*6 = 36 Mbps
Max. data rate = 2B log2V bits/sec
Notes: These are fundamental limits; real systems can only approach them.
S/N is called the signal to noise ratio SNR, and it is commonly measured in decibels on a logarithmic scale e.g., 10dB means the signal is 10X noise, 20dB means 100X noise, etc.

## Slide 22: Maximum Data Rate of a Channel
Shannon's theorem relates the data rate to the bandwidth (B) and signal strength (S) relative to the noise (N):
Max. data rate = B log2(1 + S/N) bits/sec
SNR: Represents the difference in decibels (10*log10S/N) between the received signal and the noise floor.
If the radio receives a signal of -75dBm and the measured noise floor is -90dBm, the SNR is 15dB.
Notes: These are fundamental limits; real systems can only approach them.
S/N is called the signal to noise ratio SNR, and it is commonly measured in decibels on a logarithmic scale e.g., 10dB means the signal is 10X noise, 20dB means 100X noise, etc.

## Slide 23: Electromagnetic Spectrum (2)
To manage interference, spectrum is carefully divided, and its use regulated and licensed, e.g., sold at auction.
Source: NTIA Office of Spectrum Management, 2003
3 GHz
30 GHz
3 GHz
300 MHz
WiFi (ISM bands)
Part of the US frequency allocations
Notes: TV, cellular, satellite frequencies are heavily regulated.

## Slide 24: Electromagnetic Spectrum (3)
Fortunately, there are also unlicensed (“ISM”) bands:
    Free for use at low power; devices manage interference
    Widely used for networking; WiFi, Bluetooth, Zigbee, etc.
802.11
b/g/n
802.11a/g/n
Notes: These bands are used for WiFi, etc., not for cellular.

## Slide 25: Radio Transmission
In the HF band, radio waves bounce off the ionosphere.
In the VLF, LF, and MF bands, radio waves follow the curvature of the earth
Radio signals penetrate buildings well and propagate for long distances with path loss
Notes: The path loss makes the signal fall of at least as fast as 1/d^2 due to the RF energy being spread out over a greater region.

## Slide 26: Distance and packet loss rate